## Slide 1
Methylene Chloride (DCM) Training
OKLAHOMA STATE UNIVERSITY
(405) 744-7241
Created October 2025

## Slide 2
OBJECTIVES
What is methylene chloride
Physical and health hazards
Regulations under the Environmental Protection Agency’s (EPA) Toxic Substance Control Act (TSCA)
Compliance at OSU

## Slide 3
WHAT IS METHYLENE CHLORIDE?
Dichloromethane, or DCM, is also known by its common name: methylene chloride (CAS #75-09-2). DCM is a colorless liquid and a volatile chemical with a sweet odor. The solvent is used in a variety of consumer and commercial applications, including adhesives and sealants, automotive products, and paint and coating removers.

## Slide 4
Physical & Health Hazards

## Slide 5
PHYSICAL HAZARDS
If significantly heated, DCM vapor can combust, generating toxic fumes.
Use dry chemical, CO2, water spray or foam as extinguishing agents.
DCM vapors are heavier than air. This can cause localization of vapors at ground-level when spilled.

## Slide 6
HEALTH HAZARDS: EXPOSURE
Primary routes of exposure are skin contact and inhalation, but DCM can be absorbed through the eyes and through injection.
Exposure carries both acute health effects from large, short-term exposures, and chronic health effects from repeated exposures over time.

## Slide 7
HEALTH HAZARDS: ACUTE EXPOSURE
Contact can cause numbness and severely irritate and burn the skin and eyes with possible eye damage.
Inhaling DCM can irritate the nose, throat and lungs, causing coughing, wheezing and/or shortness of breath.
Higher exposure can cause headaches, nausea, fatigue, dizziness, lightheadedness, weakness, unconsciousness, coma, and even death.

## Slide 8
HEALTH HAZARDS: CHRONIC EXPOSURE
DCM is a suspected carcinogen as it has been shown to cause liver and lung cancer in animals.
It may cause bronchitis to develop with coughing, phlegm, and/or shortness of breath.
It may affect the brain causing memory loss, poor coordination, and reduced thinking ability.
It can cause damage to the kidneys.

## Slide 9
EPA Regulations Under TSCA

## Slide 10
TOXIC SUBSTANCE CONTROL ACT
In April 2024, the EPA issued a final rule regulating DCM under the TSCA to protect humans from health risks such as neurotoxicity effects and cancer from inhalation or dermal exposures.
Anyone who manufactures (including imports), processes, distributes in commerce, uses, or disposes of methylene chloride or products containing methylene chloride may be impacted by the EPA’s regulation of the chemical.
This includes laboratory research use.

## Slide 11
WORKPLACE CHEMICAL PROTECTION PROGRAM (WCPP)
A Workplace Chemical Protection Program or WCPP is required for the use of DCM.
The WCPP requires that owners and operators of facilities using DCM take appropriate measures to meet new inhalation exposure limits (including 2 ppm as an 8-hour time weighted average [TWA]) and develop and implement an exposure control plan (ECP), among other requirements.

## Slide 12
WCPP TIMELINE
Distribution of DCM for consumer use has been prohibited after May 5, 2025.
Facilities must complete initial monitoring before May 5, 2025.
New facilities must complete initial monitoring with 30 days of initial use.
Facilities must ensure not to exceed the Existing Chemical Exposure Limit (ECEL) (2ppm as an 8-hr TWA) or the EPA Short-Term Exposure Limit (STEL) (16ppm as a 15-min TWA) for all potentially exposed persons by August 1, 2025.

## Slide 13
WCPP TIMELINE
Regulated areas must be established by August 1, 2025, or within 3 months of receipt of initial monitoring.
Facilities must develop and implement an Exposure Control Plan by October 30, 2025.
Periodic monitoring must be conducted at a minimum of every 5 years dependent upon initial monitoring results.

## Slide 14
REGULATED AREAS
Any area of DCM use that exceeds the ECEL or STEL must be designated as a regulated area.
Regulated areas must be marked clearly with visual boundaries and have restricted access.
Regulated areas require respiratory protection when DCM is in use. This must be a supplied air respirator or a self-contained breathing apparatus (SCBA).

## Slide 15
EXPOSURE CONTROL PLAN
The ECP must:
  Document the specific controls used to reduce exposure to DCM and justification for their use;
  Describe and define any regulated areas;
  Outline procedures for initial and periodic monitoring;
  Describe all job tasks involving DCM;

## Slide 16
EXPOSURE CONTROL PLAN
The ECP must:
  Detail the PPE required for job tasks involving exposure to DCM;
  Describe the DCM training program for all personnel working with DCM; and
  Maintain records of monitoring results.

## Slide 17
ELIMINATION OR SUBSTITUTION
Anyone with a chemical that has even 0.1% concentration of DCM is under this regulation and must comply.
Using the hierarchy of controls or the RAMP method to eliminating or substituting DCM in your procedures can eliminate the need for this compliance:
  Recognize hazards;
  Assess risks;
  Minimize and manage hazards; and
  Prepare for emergencies.

## Slide 18
CONTROLS AND RESTRICTIONS
If DCM use CANNOT be eliminated or substituted, engineering controls such as chemical fume hoods should be used.
Administrative controls should also be in place if DCM exposure is not eliminated. Some examples include:
  Restricting DCM use in teaching labs;
  Requiring the use of restricted areas;
  Required trainings; and
  Use of ECPs.

## Slide 19
PERSONAL PROTECTIVE EQUIPMENT (PPE)
For PPE, laboratory coats, safety glasses or splash goggles, and either polyvinyl alcohol gloves or double nitrile gloves must be worn.
LLDPE laminate or butyl viton gloves may be used for procedures involving strong oxidizing acids.
If initial monitoring results in exposure levels above limits, authorized personnel will need to be added to the Respiratory Protection Program before using a supplied air respirator or SCBA.

## Slide 20
Regulation Compliance at OSU

## Slide 21
ENSURING COMPLIANCE
If you are a PI on campus who uses DCM, also known as methylene chloride, in your laboratory spaces, please contact EHS to conduct air monitoring and an assessment of your current chemical hygiene plan.
Submit a DCM Storage and Usage Form to assess all usages of DCM in your space.
Standard Operating Procedures (SOPs), an ECP, and a WCPP must be created for each laboratory that uses DCM. Contact ehs@okstate.edu for templates for these forms. Assistance can also be provided in the completion of these forms upon request.

## Slide 22
ENSURING COMPLIANCE
Assistance can also be provided in the completion of the SOPs, ECP, and WCPP forms upon request.
You can visit our website at ehs.okstate.edu for more information and updates on DCM.

## Slide 23
RESOURCES
DCM Storage and Usage Form
OSU DCM Fact Sheet
CSHEMA Methylene Chloride Resources
EPA Fact Sheet: Methylene Chloride or Dichloromethane

## Slide 24
REFERENCES AND ADDITIONAL RESOURCES
FACT SHEET: 2024 Final Risk Management Rule for Methylene Chloride under TSCA
A Guide to Complying with the 2024 Methylene Chloride Regulation
EPA Fact Sheet: Methylene Chloride or Dichloromethane
Methylene Chloride Hazards for Bathtub Refinishers
Preliminary Information on Manufacturing, Processing, Distribution, Use, and Disposal: Methylene Chloride
Risk Evaluation for Methylene Chloride
Ansell Chemical Glove Resistance Guide

## Slide 25
Fire Protection Engineering
Life Safety and Emergency Preparedness
Environmental Compliance
Laboratory Safety
Occupational Safety
Occupational Health and Medical Surveillance
Materials Management
Industrial Hygiene
Chemical Hygiene
Safety Training
PROGRAMS AND SERVICES
ENVIRONMENTAL HEALTH AND SAFETY

## Slide 26
Questions?

## Slide 27
O | 405.744.7241
E | ehs@okstate.edu
1202 W. Farm Road
ehs.okstate.edu
Contact Information
Environmental Health and Safety