## Slide 1
GROUNDS SAFETY
Oklahoma State University
(405) 744-7241
Current as of May 2025

## Slide 2
OBJECTIVES
General Grounds Safety
Terms needed for mowing
Pre-Operations Checks
Personal Protective Equipment
Operating Procedures
Trimming and Cutting Equipment
Thrown Objects

## Slide 3
GETTING STARTED
Oklahoma State University takes pride in our beautiful grounds, so it only makes sense to keep our expert employees safe.
Not everyone knows how to operate landscaping equipment safely. Common accidents include lacerations, injuries from projectiles, burns, electrical shock, strains and slips, trips, and falls.
The purpose of this training is to help you become familiar with grounds equipment. Let's get started.

## Slide 4
GENERAL GROUNDS SAFETY
Always read the owner’s manual before operation and beginning work with a piece of equipment. Familiarize yourself with controls and safety equipment.
Inspect the work area prior to starting work. Look for hazards such as rocks, stakes and sprinkler heads. Always stop work if a pedestrian enters the work area. Never leave equipment unattended.
Always remove a piece of equipment from service immediately if maintenance is required.
Ensure that all guards and safety switches are working properly, are in place and in good condition.

## Slide 5
GENERAL GROUNDS SAFETY
Always wear sunscreen while working outdoors.
Be careful to avoid fatigue and heat stress by taking breaks and drinking plenty of water.
Never operate equipment if you’re tired, sick or taking medication.
Take special precautions when working with electrical equipment. Avoid accidentally cutting any extension cords with equipment.

## Slide 6
TERMS USED IN THIS TRAINING PROGRAM
Power Take Off (PTO)
  PTO is the area of the machine where rotating torque is directly transferred to another machine or tool. In the mower case, the rotating torque is used to turn the mower blades.
Roll Over Protection System (ROPS)
  ROPS is attached to some vehicle frames to help prevent the vehicle from upsetting more than 90 degrees and prevent the occupant from being crushed if an upset does occur.
Deadman Switch
  A device that will automatically turn the machine off if the operator should leave the driver's seat for any reason. It may also be used in the case of an equipment malfunction to turn the machine off.

## Slide 7
REMEMBER
Roll Over Protection System (ROPS)
Trivia #1: Although there are few accidents with mowers, several injuries occur when mowers are in use. These accidents are caused by driving too fast, operating unsafely on uneven ground, operating a mower that has not been mechanically maintained, and pushing the mower beyond safe operating limits.
Please wear your seat belt even when ROPS protection is provided.

## Slide 8
PRE-OPERATION PROCEDURES
If problems can be identified before stepping into the driver's seat, accidents can be prevented, and the equipment will remain properly maintained.
Pre-Operation procedures can be broken down into three areas:
Before operating the mower, walk around the area that needs to be mowed
Guidelines for getting familiar with your equipment
Using a safety checklist
Personal protective equipment

## Slide 9
PRE-OPERATION PROCEDURES
Guidelines for getting familiar with your equipment:
Read the operator’s manual first
Make all necessary adjustments before turning on the machine
Observe and question a skilled operator until comfortable with procedures
Practice operating in an open area first

## Slide 10
REMEMBER
Observe and question a skilled operator until you are comfortable with the procedures.
Trivia #2: Overturns have the highest fatality rate for unintentional injuries involving tractors that occur on the farm, according to reports from 31 states covering about 66% of the farm tractors in the United States. In 1995, overturns accounted for 55% of all on-the-farm fatalities reported, with an annual rate of 5.5 deaths per 100,000 tractors.(National Safety Council Accidents Facts, p137).

## Slide 11
SAFETY CHECKLIST
Make sure all protective guards are in place. Never remove guards.
Determine that steering is responsive before beginning a job
Test the brakes
Clean the steps and operating platform to prevent slipping
Ensure that tires are properly inflated

## Slide 12
SAFETY CHECKLIST
Check for correct tightness of bolts
Ensure a Slow-Moving Vehicle (SMV) sign is installed and visible
Ensure flashing warning signs are present and operating when traveling on roadways
Once installed, never remove guards, lights or signs. Ignoring these simple items can cause accidents.

## Slide 13
REMEMBER
Never remove guards, flashing lights or Slow-Moving Vehicle signs—even if they are bothering you.
Trivia #3: Private industry reported 2.8 million non-fatal injuries and illnesses among mowers during 2019, which is unchanged from 2017 and 2018. This is reported form the U.S. Bureau of Labor Statistics.

## Slide 14
PROTECTIVE GEAR
Hearing protection, such as earplugs or muffs, are required for prolonged noise exposure.
Gloves can't always prevent a finger amputation, but they can guard against cuts, abrasions, chemicals and other skin irritants. Wear gloves that fit and wear the right type of glove for the job.
Long pants should be worn to protect against hazards such as flying debris, skin irritants and burns from exhaust.

## Slide 15
PROTECTIVE GEAR
Dust masks reduce inhalation of dust and other particles in the air. Do not use when working with chemicals, toxic gases, and or when there is an oxygen deficiency.
Safety glasses should be worn with side shields. If you wear glasses, ensure they have impact-resistant lenses.

## Slide 16
PROTECTIVE GEAR
Remember to wear the right type of personal protective equipment for the job, keep the items clean and sanitary, and replace any items that wear out or become broken.

## Slide 17
REMEMBER
Wear personal protective equipment for ears, eyes, hands, nose, legs and feet.
Keep the items clean and sanitary.
Trivia #4: Most Mower accidents occur between April and October, with June being the peak accident month.

## Slide 18
OPERATING PROCEDURES
There are 3 kinds of procedures for safely operating grounds equipment:
General Safety Procedures
Operating on Uneven Ground
Avoiding Thrown Object Hazards

## Slide 19
GENERAL SAFETY GUIDELINES
Only the operator is allowed on the equipment. No passengers allowed!

## Slide 20
GENERAL SAFETY GUIDELINES
When leaving the seat, the operator should disengage the PTO, engage the brake, stop the engine, and wait for all parts to stop before dismounting.
The operator should not adjust any mechanism of the equipment while the mower is running but should follow the above procedures making sure all parts have stopped moving.

## Slide 21
GENERAL SAFETY GUIDELINES
When driving between mowing jobs, crossing a road, path or sidewalk, or when not using the mower, the operator should disengage the PTO to stop the mower blade.
Operators should not mow in conditions where traction or stability is questionable. If uncertain, test drive a section with the PTO off.

## Slide 22
REMEMBER
Disengaging the Power Take Off (PTO), putting on the brake, stopping the engine, and waiting for all parts to stop moving before getting off the mower, are good common-sense rules to follow.
Trivia #5: Over half of tractor/mower-related deaths result from overturns. Most go over sideways; some go over backward. Chances of survival are better if your tractor/mower is equipped with a rollover protective structure (ROPS) and a seat belt.

## Slide 23
GENERAL SAFETY GUIDELINES
Never refuel equipment while the engine is running or extremely hot. A fire or explosion could result.

## Slide 24
SAFE FUELING PROCEDURES
Always refuel in a well-ventilated area on concrete or pavement. Never refuel equipment in grassy areas, as sparks could cause a fire.
Before refueling equipment that has recently been used, allow the engine to cool before adding gasoline.
Never smoke around gasoline or gasoline powered equipment.
Always clean gasoline spills immediately to avoid accidental ignition.

## Slide 25
OPERATING ON UNEVEN GROUND
Operating on uneven ground is the number one cause of accidents due to rolling of the machine. Since not all machinery is equipped with ROPS, mower operators have been killed or severely injured by improper operation on uneven ground.
Even when ROPS is used, operators remain at risk and therefore should evaluate each situation on the safest way to mow.
If ROPS is on the machine wear your seat belt, equipment not have ROPS do not wear a seatbelt.

## Slide 26
OPERATING ON UNEVEN GROUND
If an area is too sloped or the ground is deemed too uneven to operate the mower safely, use a weed eater or push mower.

## Slide 27
OPERATING ON UNEVEN GROUND
Before mowing on EVEN ground, prepare the machine:
Lock the differential for better traction on slopes and in slippery places.
If available, install rear and/or front wheel weights to increase stability, steering, and traction. Refer to the machine's operating manual for installing these.

## Slide 28
OPERATING ON UNEVEN GROUND
When mowing on UNEVEN ground:
Slow down the travel speed so that you can see and react to hazards in your path. Overturns are four-times more likely to occur when travelling faster than mowing speed.
Be on the alert for holes and ditches covered by grass or debris. A wheel may drop and cause an overturn.

## Slide 29
OPERATING ON UNEVEN GROUND
When mowing on UNEVEN ground:
Drive up and down a hill, not across.
Do not stop when going up hill or down hill. If the mower stops going up hill, turn off the PTO and back down slowly.
Do not try to stabilize the mower by putting your foot on the ground.
If in doubt, do not mow on uneven ground
Saving yourself time by operating in an unsafe situation could cost you life or limb.

## Slide 30
REMEMBER
When operating, maintain a 5-foot buffer zone from drop-offs. String trimmers or push mowers should be used
Trivia #6: The fewest mower accidents occur on Sunday. On the other hand, Saturday and Wednesday are the peak days for accidents. Keep in mind that accidents can and do occur on any day of the week, usually when they are least expected.

## Slide 31
TRIMMING AND CUTTING EQUIPMENT
Before transporting any equipment, ensure it is turned off.
Always carry equipment with cutting mechanisms away from the body.
Always keep hands and feet away from blades and cutting heads.
Never attempt to cut anything above shoulder height.
Always use two hands and maintain a good grip on equipment.
Use shoulder harnesses to prevent strain from overexertion.

## Slide 32
THROWN OBJECT HAZARDS
Since most newer model mowers now have optional equipment that catches cut material, it is less important than it once was for operators to be aware of thrown object hazards.
However, many mowers without the optional equipment are still in use. This makes it necessary for all operators to be aware of and control for these hazards.
If bystander is hit during mowing please report to your supervisor.

## Slide 33
THROWN OBJECT HAZARDS
To avoid these hazards . . .
Operators should check areas where grass and weeds are high enough to hide debris that could be struck and thrown. The area should be closely inspected before mowing and these objects collected.
Areas with high grass and weeds should be mowed to an intermediate height, inspected a second time, then mowed again to the desired height.

## Slide 34
THROWN OBJECT HAZARDS
To avoid these hazards . . .
Operators should estimate how far and in what direction objects may be thrown
Equipment shields must remain in place and not be removed. The shields help prevent objects from being thrown
Operators must recognize the throwing capabilities of the equipment being used and follow all guidelines to ensure safety of the people, animals, equipment, and the operator.

## Slide 35
REMEMBER
First walk and check areas to be mowed, looking for and removing objects that might be thrown.
Trivia #7: The Deadman Switch is referred to by mower operators and is a device that will automatically power-off machinery or equipment if the operator should leave the driver's seat for any reason.

## Slide 36
LINE TRIMMERS
Remove all projectiles before trimming.
Watch out for exposed electrical wires, communication lines, that could be damaged by the trimmer string.
Don’t remove protective guards and string guides.
Monitor the string length this might cause the string to strike you unexpectedly.
Make sure all bystanders are out of the way before you begin trimming.
Use body harness to support line trimmer.

## Slide 37
LINE TRIMMERS
Wear appropriate protective clothing and equipment such as long-pants, long-sleeve shirts, gloves, hard boots, goggles or safety glasses, face shield and ear plugs.
Turn off gas-powered trimmers before inspecting, cleaning, adjusting, replacing string or leave unattended.
Before refueling gas-powered trimmers, place the trimmer on the ground and allow the engine to cool.

## Slide 38
LAWN EDGER
Make sure bystanders are clear before starting the edger.
Don’t start an edger if the blade is touching the ground. It could move unpredictably and possibly contact your feet and legs.
Wear appropriate eye protection such as goggles or safety glasses to guard against flying objects.
Do not stand in front of lawn edger while it is running.

## Slide 39
LAWN EDGER
Don’t remove protective guards or shields.
Operate the edger at full blade speed.
When edging along roadways wear reflective vest, stay as close to the curb as possible to avoid being hit by passing vehicles.
Turn off a gas-powered edger running while inspecting, cleaning, adjusting, or replacing the blade unattended.
Ensure bystanders are clear from the area when starting and operating.

## Slide 40
LEAF BLOWER
Make sure bystanders are clear before starting the leaf blower and when operating.
Always wear eye protection when operating a leaf blower even small stones can blind a person.
Hearing protection is recommended.
Always start and run the unit in an upright position.
Never operate the blower without the tubing.

## Slide 41
LEAF BLOWER
Always direct the debris away from people, animals, glass and solid objects that could cause the debris to rebound or ricochet.
Never use the blower to spread or mist chemicals, fertilizers or other toxic substances.
Never use the blower from ladders, trees, rooftops or other unstable surfaces.
Never blow debris directly at bystanders.

## Slide 42
TAKEAWAYS
Importance of Pre-Operation Checks
The right PPE for the job
Walk the ground first
Watch out for people
Safety Devices never bypass

## Slide 43
Fire Protection Engineering
Life Safety and Emergency Preparedness
Environmental Compliance
Laboratory Safety
Occupational Safety
Occupational Health and Medical Surveillance
Materials Management
Industrial Hygiene
Chemical Hygiene
Safety Training
PROGRAMS AND SERVICES
ENVIRONMENTAL HEALTH AND SAFETY

## Slide 44
This project was completed as part of a graduate training course in Instructional Systems Design at Oklahoma State University, in collaboration with Oklahoma State University Environmental Health & Safety. Technical support was provided by Oklahoma State University Edmon Low Library.

## Slide 45
O | 405.744.7241
E | ehs@okstate.edu
UHS Suite 002
ehs.okstate.edu
Environmental Health & Safety
Oklahoma State University

## Slide 46
QUESTIONS?